## Slide 1: Strategies for Fault Tolerance Using DDS
Paul Schmitt
Real-Time Innovations Field Application Engineer

## Slide 2: What Is Fault Tolerance?
Fault Tolerance is the ability of a system to continue operating, with little or no degradation in service, in the face of a fault (Ideally, hardware failure or software bug)
Fault Tolerance is a “game of statistics”, in that one needs to Detect the failure and …
  Switchover to the Backup to continue ”correct” operation.
  Repair the fault within a set Mean Time To Repair (MTTR)
    Meaning that: The likelihood of a second fault with in the MTTR is acceptable (i.e., not likely)

## Slide 3: Requirements of Fault Tolerant Approaches (1/3)
Distributed
  Especially in a hostile environment, a Single Fault can be the result of fire, flood, or explosion.
Isolated
  One fault MUST not be allowed to cascade to the backup or standby units (i.e., create a second fault)

## Slide 4: Requirements of Fault Tolerant Approaches (2/3)
End-to-end
  Controllers, Actuators, and the Network must be redundant
Timely Detection of Faults in both Primary and Backup Systems
  A backup system failing means the system is effectively running simplex (with a fault) until the primary component fails.
    Comes back to MTTR and acceptable risk of a second failure
  “Timely / Time” is dependent upon YOUR applications requirements and Mission Criticality

## Slide 5: Requirements of Fault Tolerant Approaches (3/3)
Timely Switchover to Standby and Standby Roles
  “Switchover time” Includes detection, and the Switchover itself (i.e., the time for the Backup or Standby to assume full Primary duties.)
  Hot Standby, Warm Standby, Cold Standby
    These represent the level of ”readiness” and relatively increase in time required for the backup to take on the Primary role.
Repairable / Field Replaceable Unit (FRU)
  MTTR = Fault Detection time + Repair time
  To minimize MTTR, usually requires ”hot” replacement (i.e., while the system is operating)
  Repair – for software fault, can mean (temporarily) reboot.

## Slide 6: Approaches to Redundancy
Simple Duplex Controllers
  DDS Ownership Strength Primary and Backup
Three-way Voting
  DDS Ownership Strength Primary, Secondary, Tertiary
Three-way Selected Sample – sample by sample “voting”
  No Roles, no Ownership strength (shared ownership)
    All three controllers send samples equally
  Actuator selects DDS sample based on majority agreeing sample
Hardware - so called ”Pair & Spare” (for completeness)
  Does not use DDS for Redundancy
Notes: Approach 2 can be a superset of Approach 1 in that we can allow just 1 or two controllers to boot if three are not detected within a start up window

## Slide 7: Simple Duplex Redundant Controller
Set Roles w/Thrust Command Ownership Strength
  Switchover time based on Deadline, not Ownership Strength intensification time
Backup Strength intensifies to guard against zombie Primary
Port Side Thrusters
Helm Controllers
Connext Databus
Backup
Primary
Heartbeat
Thruster 1 & 2 Commands

## Slide 8: Simple Duplex Redundant Controller Attributes
Guards against a hardware and limited software failures.
  Some protection against zombie process on Primary
Does not guard against secondary incorrectly assuming Primary Role
  Software Bug
  Loses contact with heartbeat
    Note: you may want this behavior if system communications link is severed to allow each controller to control its link segment
System needs to be reset to recover original Primary in Primary role
  ownership strength will eventually rollover

## Slide 9: Three-way Voted Redundant Controller
Set Roles w/Thrust Command Ownership Strength
Role is voted for with Majority Vote wins
Switchover time based on Deadline, independent of Voting time
Port Side Thrusters
Helm Controllers
Connext Databus
Secondary
Primary
Heartbeat
Thruster 1 & 2 Commands
Tertiary
Vote
Heartbeat
Vote
Secondary
Primary

## Slide 10: Three-way Redundant Controller Attributes
Guards against hardware and limited software failure
  Can also guard against zombie Primary process failure
Guards against secondary or tertiary unilaterally assuming control (software bug)
  Although requiring a majority vote, Limits but does not eliminate, Secondary or Tertiary increasing ownership strength anyway
  Loses contact with heartbeat
    Note: you may want this behavior if system communications link is severed to allow each controller to control its link segment
Software is moderately more complex
  Software Voting algorithm (leverage Redundancy Layer from GitHub)
Can combine with Backup Role Strength Intensification to guard against Zombie Primary

## Slide 11: Three-way Selected Sample
Shared Ownership / No Controller Roles
Actuator/Thruster selects majority Sample
  Sets alarm if a minority sample detected
Heartbeat used to alarm system (MTTR)
Port Side Thrusters
Helm Controllers
Connext Databus
Heartbeat
Controller 3
Heartbeat
Controller 2
Controller 1

## Slide 12: Three-way Selected Sample Attributes
Guards against hardware failure and software Bugs
  Assuming each controller software written by a different vendor (Guards against the same bug being hit on all three controllers at the same time)
  NASA did this with the Space Shuttle
Requires more time to process each sample at the Actuator
Software is moderately more complex
  Software Selection algorithm (leverage Redundancy Layer from GitHub)

## Slide 13: Hardware – “Pair and Spare”
No Primary or Secondary Role
Two Processors on each controller, clock-to-clock comparison
Bus disconnected within one bus clock cycle if comparison fails
Port Side Thrusters
Helm Controllers
Connext Databus
Thruster 1 & 2 Commands
Controller 2
Controller 1
=
=
≠
Notes: Really guards against Hardware failure – limited software protection if Check-pointing to a transactional data-base is perfromed

## Slide 14: Summary
Redundancy Architecture | Cost | Complexity | Detect and overcome Hardware Fault | Detect and overcome Software Fault | Distributed | Switching Time (backup to primary)
Simple Duplex | Lowest | Lowest | Yes | Minimal, Total failure & Zombie Primary | Yes | Deadline based
Three-way voting | Low | Low* | Yes | Better, Basic software integrity checked by vote | Yes | Deadline based
Three-way Selected Sample | Low | Highest (multivendor) | Yes | Yes | Yes | N/A - Per sample selection (Impact performance)
Hardware “Pair & Spare” | High | High / custom hardware | Yes | No | No | Fastest (One CPU / Bus Clock cycle)
* Redundancy Layer code can be leveraged from GitHub minimizing new development

## Slide 15: Demo

## Slide 16: Three-way Voting Pixytracker Demo
Also supports Simple Duplex Redundancy
  Runs with 1, 2 or 3 Tracker Apps
  Code here

## Slide 17: Demo Layout

## Slide 18: DDS Mechanisms Discussed
DDS Mechanism | Component Used | Description
Liveliness | Controller Components | Detects a redundant component / participant failure
Ownership | Between Controller and Actuator | Enables the receiving application, independent of the redundancy strategy used to see at most two samples (one on each bus A and B)
Key’d data | Controller Components | Enables redundant components to use liveliness to detect each controller in a 3-way voting system
Match on Publisher | Controller Components | Enables the system to determine how many controllers are active.
Durability | Controller Components | Allows a so called “Late Joiner” to be a part of a running system. This may include obtaining system state or a number of previous samples to integrate to quickly get within the acceptable error value to become a Hot Standby.
Explicit Application Level Acknowledgement | Controller Components | Discussed above, but not suitable for this application due to the fact that only one heartbeat instance is sent from each controller causing head-of-line blocking (and we have full duplex heartbeats)

## Slide 19: Thank You!
Paul Schmitt
paul.schmitt@rti.com
LinkedIn: www.linkedin.com/in/paul-schmitt-mass